## Slide 1
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District
BUILDING STRONG®
U.S. ARMY CORPS OF ENGINEERS | Jacksonville District
Presented by:
Jason Harrah, Project Manager, USACE, Jacksonville District
Steve Schropp, Senior Scientist, Taylor Engineering, Inc.
October 25, 2012
JACKSONVILLE HARBOR DEEPENING STUDY ECOLOGICAL AND WATER QUALITY MODELING

## Slide 2: ECOLOGICAL MODELING STUDY TEAM
U.S. ARMY CORPS OF ENGINEERS (USACE)
  Jason Harrah (PM)
  Steven Bratos P.E., Senior Engineer
  Paul Stodola, Senior Biologist
  Mike Hollingsworth, Senior Biologist
TAYLOR ENGINEERING
  Steven Schropp, Ph.D. (PM)
  David Stites, Ph.D.
  Michael Kabiling, Ph.D., P.E.
2

## Slide 3: STUDY OVERVIEW
Jacksonville Harbor is located in Duval County beginning at the mouth of the St. Johns River where it joins the Atlantic Ocean
The harbor provides access to deep draft vessel traffic using terminal facilities located in the City of Jacksonville
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District
3

## Slide 4
JACKSONVILLE HARBOR STUDY
AREA
MILE POINT
BLOUNT ISLAND
MAYPORT NAVAL STATION
MILL COVE
BUCK ISLAND
Segment 1
FOCUS OF CURRENT STUDY
JPA TALLEYRAND
TERMINAL
MAYPORT
50’
FORT
GEORGE
ISLAND
OIL TERMINALS
JEA
FUEL DOCK
BARTRAM ISLAND
DREDGED MATERIAL
SITES
BEACH QUALITY
DREDGED
MATERIAL
PLACEMENT
U.S. NAVY FUEL DEPOT
OIL TERMINAL
OIL TERMINAL
JPA TERMINALS
BUCK ISLAND
JPA DAMES POINT TERMINALS
Segment 2
Mile 20
Segment 3
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District
Authorized Depths
Segments 1 and 2: 40 feet
Segment 3: 38 feet
JEA COAL
4
Mile 13

## Slide 5: STUDY GOALS
Provide transportation costs savings
Develop most cost-effective means for placement of dredged material (over 50-year project life)
Accommodate existing and larger commercial ship traffic while minimizing impacts to environmental resources
5
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District
Notes: Provide transportation costs savings associated with draft restrictions to the existing authorized channel depth
Develop the most cost-effective means for disposal of dredged material over the 50-year project life
Identify the best plan that minimizes impacts to environmental resources and accommodates existing and larger commercial ship traffic
1. Transportation delays occur due to the existing conditions at Jacksonville Harbor. Vessels are restricted to the maximum depth of 40 feet, authorized project depth. Larger vessels must light-load or wait for tidal advantage to transit Jacksonville Harbor. This causes increased transportation costs. The 40-foot project depth impacts the introduction of larger vessels into the fleet. These impacts create transportation inefficiencies. Larger vessels are restricted to limited turning areas.

## Slide 6: AGENCY AND PUBLIC COORDINATION EFFORTS TO DATE
May 2007: First Public Scoping Letter
February 2008: Feasibility Scoping Meeting
May 2009: Second Public Scoping Letter
  May 2009: Public Workshop on Project Scope
  March 2012: Interagency Meeting on Ecological Modeling
May 2012: Public Meeting on Ecological Modeling
July 2012: Initiated Monthly Interagency and Bi-Monthly Public Teleconferences
6
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District

## Slide 7: ANTICIPATED FUTURE INTERAGENCY AND PUBLIC MEETINGS *
Oct 2012: Ecological Modeling Preliminary Results Interagency and Public Meetings (Now)
November 2012: Agency Mitigation & Monitoring Planning Meetings
December 2012: Ecological Modeling Draft Report Interagency Meeting
Feb 2013: Rock Removal (Blasting) Public Meeting
  May 2013: Draft Feasibility Report/Supplemental Environmental Impact Statement Public Meeting
Oct 2013: Final Feasibility Report/Supplemental Environmental Impact Statement Public Meeting
Monthly Interagency and Bi-Monthly Public Teleconferences
http://www.saj.usace.army.mil
* Study Updates and Public Participation Opportunities on Study Website
7
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District

## Slide 8: STUDY SCHEDULE (President’s Initiative)
April 2013: Draft Feasibility Report w/SEIS Complete
May 2013: Public Review Period
Oct 2013: Final Feasibility Report w/SEIS Complete
April 2014: Chief of Engineers Report
July 2014: ASA Letter to Congress and Record of Decision
TBD: Authorization Bill
8
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District

## Slide 9: ECOLOGICAL MODELING OVERVIEW
Purpose
  Support National Environmental Policy Act assessment
Study Area
  River mouth to Lake George
  Deeper channel could increase tidal exchange and cause:
    Higher salinity in river
    Changes in water circulation and residence time
Palatka
Buckman Bridge
Shands Bridge
Mayport
Jacksonville
Lake George
9

## Slide 10: ECOLOGICAL MODELING OVERVIEW
Potential effects of salinity and circulation changes
  Wetland communities shift location and acreage
  Loss of eelgrass habitat and shift in habitat location
  Shifts in location of optimal fish salinity ranges and related changes in habitat availability
  Loss of low-salinity benthic macroinvertebrate (e.g., shrimp, crab, clams, mussels, worms) habitat and shift in habitat range
  Changes in plankton blooms and resulting dissolved oxygen
St. Johns River Water Management District Water Supply Impact Study provides ecological model framework
10

## Slide 11: ECOLOGICAL MODELING OVERVIEW
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District
EFDC Model
Water circulation and salinity
Ecological Models
  Wetland vegetation
  Submerged aquatic vegetation (eelgrass)
  Benthic macroinvertebrates (shrimp, crab, clams, mussels, worms)
  Fish
  Plankton
Water Quality Model
  EFDC/CE-QUAL-ICM
11

## Slide 12
EFDC CIRCULATION AND SALINITY MODEL
Model conditions and inputs
  4,824 cells, 6 vertical layers
  Ocean water level
  Rainfall and Evaporation
  Wind
  Salinity
  Lateral inflows
  1995 land use
12

## Slide 13
The 3-year period, 1999 - 2001, is lowest 3 consecutive year flow in the 78 year record
Chart: 
| 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
LSJR Gaged Annual Q (cfs) (75 %) | 3778.8152 | 4936.0213 | 9797.6089 | 8387.8385 | 4797.9704 | 8507.3282 | 3085.5875 | 3868.5561 | 3673.1874 | 6723.0069 | 7946.9524 | 6177.2318 | 9931.5237 | 5564.5157 | 2270.0847 | 5474.924 | 7082.2527 | 4895.5248 | 2329.3167
Evaluation Period
Discharge (cfs)
Year
LOWER ST. JOHNS RIVER ANNUAL FLOW
13

## Slide 14
Shands Bridge
Buckman Bridge
Acosta Bridge
Dames Point Bridge
River Mouth
EFDC RESULTS
  Baseline at 40-foot project depth - salinity profile
14

## Slide 15: WETLAND VEGETATION MODEL
Evaluation Topic
  Wetland (marsh, swamp) shift due to salinity change
  Evaluation Method
  Wetland boundaries defined by salinity “break points”
  Modeled salinity movement predicts community boundary and areal change
15

## Slide 16: WETLAND VEGETATION MODEL
Salinity Breakpoints
Current Condition
16

## Slide 17: WETLAND VEGETATION MODEL
Salinity Breakpoints
50-year Horizon
17

## Slide 18: SUBMERGED AQUATIC VEGETATION (SAV) MODEL
Evaluation Topic
  Salinity stress on eelgrass
Evaluation Method
  90-day average salinity
  Individual model cells
  Total area affected
18

## Slide 19
SUBMERGED AQUATIC VEGETATION (SAV) MODEL
19

## Slide 20
SUBMERGED AQUATIC VEGETATION (SAV) MODEL
20

## Slide 21: BENTHIC MACROINVERTEBRATE (BMI) MODEL
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District
Evaluation Topic
  BMI habitat area and BMI abundance
Evaluation Methods
  Changes in area (acres) and location of salinity zones
  Changes in duration and level of salinity (Partial Duration Frequency Analysis – PDFA)
  Total BMI abundance
21

## Slide 22
BMI SALINITY ZONES MAX 30-D, 1997
22

## Slide 23
Preliminary Results
  Small changes in maximum river bottom salinities, and corresponding small changes in BMI abundance
  Elevated salinities occur primarily between Fuller Warren Bridge and Shands Bridge
  Salinity zones affected less by deepening than by year to year changes in river flows
  Changes expected with 50 years of projected sea level rise and 155 million gallons per day (mgd) water withdrawal exceed effects of different channel depths
BENTHIC MACROINVERTEBRATE (BMI) MODELS
23

## Slide 24: FISH MODEL
Evaluation Topic
  Fish Habitat area
  Evaluation Methods
  Changes in area of each salinity category
  Changes in SAV cover
  Fish species require various salinity levels for different stages in their life cycle
24

## Slide 25
FISH MODEL
Preliminary Results
  Modeling results of the study alternatives depict minor upstream shifts in salinity zones
  Salinity zones affected less by deepening than by year to year changes in river flows
  These preliminary results indicate that fish habitat within the main stem of the river would not be adversely impacted
  Analysis is ongoing for potential effects on fish habitat within the tributary and marsh areas
25

## Slide 26: PLANKTON MODELS
Evaluation Topics (algal bloom metrics)
  Marine algal blooms
  Nitrogen (N) loading via N2-fixation
  Freshwater bloom magnitude (chlorophyll-a maximum/dissolved oxygen minimum)
  Freshwater bloom duration
Evaluation Method
  Regression models based on water age
26

## Slide 27
PLANKTON MODELS
Preliminary Results
  Preliminary results are inconclusive
  Evaluation and analysis is ongoing
27

## Slide 28: WATER QUALITY EVALUATION
Evaluation Topics
  Chlorophyll-a (for comparison to plankton empirical model)
  Dissolved Oxygen (relative to TMDL)
Evaluation Method
  EFDC Model
  CE-QUAL-ICM Model
28

## Slide 29
EFDC-CEQUAL-ICM Model Mesh
Model conditions
2,707 cells, 6 vertical layers
Model output variables
  Water surface elevation
  Velocity
  Salinity
EFDC output delivered to CEQUAL-ICM water quality model
Model is calibrated and alternative runs are in-progress
AIWW
Atlantic Ocean
St. Johns River
Crescent Lake
Lake George
29

## Slide 30
PRELIMINARY RESULTS SUMMARY
Circulation model effectively simulates water movement, elevation and salinity
The ecological models indicate some effects with study alternatives (including the no action alternative)
Preliminary effects appear greatest for SAV and wetlands
Effects due to sea level rise and water withdrawal at 50-year horizon generally exceed initial effects of any study alternative
Additional alternative simulations and analysis are underway or planned
30

## Slide 31: JACKSONVILLE HARBOR DEEPENING STUDY WEBSITE WWW.SAJ.USACE.ARMY.MIL
31

## Slide 32
QUESTIONS?
BUILDING STRONG®
US ARMY CORPS OF ENGINEERS | Jacksonville District
Certain photos courtesy of the St. Johns River Water Management District and JAXPORT.
32